## Slide 1: TeaBot
Tea Plantation Preservation Using an Intelligent Robot

## Slide 2
TeaBot is a well developed autonomous robot to replace the human resource
Watering and fertilizing for tea estates. (Liquid fertilization)
Operate in off road conditions
No need a highly arranged clear paths to navigate.
Increasing the efficiency and decrease the water and fertilizer wastage.
TeaBot can identify the path to navigate and identify the end of the plant stems and liquid fertilizing the plants efficiently.
Introducing TeaBot…

## Slide 3
How to develop the TeaBot for the liquid fertilization process efficiently?
Research Question

## Slide 4
Objectives
Develop the robot controller of the TeaBot to navigate in off-road conditions with the computer vision guidance.
The development of the image segmentation model to navigate the robot automatically in the tea plantation rows in varying environmental conditions
Develop an image processing algorithm to precisely identify the end of the tea stem and pass the coordinators to the liquid spraying controller.
Develop the liquid nozzles controller of the TeaBot to liquid fertilize the tea plants more efficiently.

## Slide 5
System Overview Diagram

## Slide 8
Robot Operating System
Why we use ROS? | Without ROS
Cooperate the components with low coupling and reduce the dependencies | have the possibilities to communicate the components
Can create the components separate. Each component is called as a node | Difficult to update the components since it has no proper convention to cooperate
nodes are communicating with ROS topics to send and receive data among the components | In programming, called it as low coupling high cohesion
Nodes are performing as publisher and subscriber | reduce the dependency level of the components
similar to the process of MQTT protocol | 
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 10
What is liquid fertilization?

## Slide 12: Budget
Item | Quantity | Amount (LKR)
Rubber wheels | 4 | 4,000
Sprocket, chain and wheel (gear system) | 4 | 10,800
Iron frame | 1 | 15,500
Motors | 4 | 14,000
43A Motor drivers | 4 | 5,400
Raspberry Pi | 1 | 90,000
12V 65Ah battery | 1 | 45,000
12V 8Ah battery | 1 | 5,000
Camera | 3 | 15,000
Liquid nozzles | 2 | 3,000
Servo motors | 8 | 9,600
Total |  | 220,000

## Slide 13
IT19973470 | Gunawardana I.I.E | 2023-044
IT19973470 Gunawardana I.I.E Software Engineering

## Slide 14
INTRODUCTION
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 15
Background
How to drive the robot?
How to do the power management of the robot?
How to operate the robot with Raspberry Pi and Arduino?
How to operate the robot with ROS?
How will the path navigation drive the robot autonomous?
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 16: Research Question
How to navigate the TeaBot efficient in off-road conditions with the computer vision guidance and maintain the power more effective?
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 17
OBJECTIVES
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 18: Specific and Sub Objectives
Main Objective
Develop the robot controller of the TeaBot to navigate in off-road conditions with the computer vision guidance.
Sub-Objectives
  Design the robot chassis to easily drive, easy to handle and consume low power and low cost to build.
  Navigate the robot with the Twist library for the given linear velocity to go forward and backward and angles to steer.
  Read the coordinates given by the computer vision to navigate the robot in the track and manual control if needed.
  Emergency stop the robot if any hazard occurred
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 19
METHODOLOGY
System Overview Diagram
Technologies
Requirements
Work Breakdown Structure
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 20
IT19973470 | Gunawardana I.I.E | 2023-044
System Overview Diagram

## Slide 21
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 22
Twist Library
Why we use Twist? | Without Twist
Capable to provide the linear velocity and the angle to the ROS node | Have the possibilities to provide velocity and the angle by creating a custom python class
Pass the linear velocities for the x, y, z directions | But arising problems when connecting the nodes because of custom classes.
Pass the angles for the x, y, z directions | Not maintaining a convention to communicate among nodes
Robot controller’s data in and out are defined by the Twist library | 
Can create a separate node with Twist library to provide the linear and angles to the robot controller | 
No need to change any coding level of the robot controller | 
Twist is a convention | 
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 23: Technologies
Technologies
Python
ROS Noetic
Algorithms
Twist to PWM
Motor Control
Angular
Ubuntu 20.04
MQTT
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 24: Requirements
IT19973470 | Gunawardana I.I.E | 2023-044
Functional Requirements
Non-Functional Requirements
  Efficient
  Easy to handle
  Navigate the robot forward and backward
  Driving the robot with the computer vision coordinates
  Capability of hazards identification
  Drive the robot in manual mode
  Performance

## Slide 25
Work Breakdown Structure
Robot Controller
Motor Controller
Make the robot structure
Autopilot
Provide computer vision coordinates
Remote Controller
Hazard Identification
Make the hardware
IT19973470 | Gunawardana I.I.E | 2023-044
Make the power supply
Create the motor driving
Twist library to linear and angular movements
Completed
To Be Completed
Angular app for remote development
Create the communication
Develop an algorithm to emergency stop
Drive
Drive the robot by providing PWM values
Drive the robot forward, backward, steer left and right
Drive it in off road conditions to test
Drive the robot with Twist library
Test the robot autopilot

## Slide 26
Evaluation
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 27
IT19973470 | Gunawardana I.I.E | 2023-044
Hardware (Robot Chassis)
6 inches wheels – 4
Wiper motors (2 to 10 amps) – 4
Bicycle sprocket wheels (18 and 16) – 4
Bicycle chains – 4
Box bar + flat iron
BTS7960 motor drivers – 4
Arduino Uno – 1
Cost – Rs. 56,300
Raspberry Pi 4 – 1
12V 65A battery
12V 8A battery
Cost – Rs. 201,300
Move forward or backward
Set the speed to drive (Twist)
Steering according to the given angles
Turn left or right while driving forward or backward (Twist)
Skid steer to left or right
Smooth driving
Optimized to protect the motors from sudden start or stop
One dedicated battery for the motors for the maximum power
Another dedicated battery for the drivers + Arduino + raspberry for a better performance
Tested in a hard environment

## Slide 28
Gantt Chart
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 29: References
[1] L. Grimstad and P. J. From, “Thorvald II - a Modular and Re-configurable Agricultural Robot,” IFAC-PapersOnLine, vol. 50, no. 1, pp. 4588–4593, 2017, doi: 10.1016/j.ifacol.2017.08.1005.
[2] Cihan YURTSEVER, Y. ERTAS, O. SUSTAM, and C. ULU, “Development of an Agriculture Robot for Row-type Seed Sowing Applications,” J. Selcuk. Spec. Issue 2020 (ICAT’20, vol. 2020, pp. 228–242, 2020.
[3] E. P. Godoy, G. T. Tangerino, R. A. Tabile, R. Y. Inamasu, and A. J. V. Porto, “Networked control system for the guidance of a four-wheel steering agricultural robotic platform,” J. Control Sci. Eng., vol. 2012, 2012, doi: 10.1155/2012/368503.
[4] P. Biber, U. Weiss, M. Dorna, and A. Albert, “Navigation System of the Autonomous Agricultural Robot ‘BoniRob,’” Work. Agric. Robot. Enabling Safe, Effic. Afford. Robot. Food Prod., pp. 1–7, 2012.
[5] T. Mueller-Sim, M. Jenkins, J. Abel, and G. Kantor, “The Robotanist: A ground-based agricultural robot for high-throughput crop phenotyping,” Proc. - IEEE Int. Conf. Robot. Autom., pp. 3634–3639, 2017, doi: 10.1109/ICRA.2017.7989418.
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 30: IT20382476 Perera P.V.Y Data Science
IT20382476 | Perera P.V.Y | 2023-044

## Slide 31
INTRODUCTION
IT20382476 | Perera P.V.Y | 2023-044

## Slide 32: Background
What is Automatic path detection?
How does Automatic path detection work?
How does Automatic Path detection help “TeaBot” to navigate ?[1][2]
How does Automatic Path Detection relate to ?[1][2]
IT20382476 | Perera P.V.Y | 2023-044

## Slide 33: Research Question
How can a suitable algorithm be created to detect the path and address TeaBot’s navigation problem ?[1][2][3][4][5]
How to design a user-friendly tangible interface to interact with children?
IT20382476 | Perera P.V.Y | 2023-044

## Slide 34
IT20382476 | Perera P.V.Y | 2023-044
OBJECTIVES

## Slide 35: Specific and Sub Objectives
Main Objective
Develop an Image Segmentation model to precisely detect the navigation path.
Sub-Objectives
  Implement a model to accurately segment the path from the background and train the Image Segmentation model using relevant training data.
  Test and validate the performance of the developed model in various scenarios, and fine-tune the model and algorithms based on feedback and performance analysis.
IT20382476 | Perera P.V.Y | 2023-044

## Slide 36
METHODOLOGY
System Overview Diagram
Technologies
Requirements
Work Breakdown Structure
IT20382476 | Perera P.V.Y.| 2023-044

## Slide 37: System Overview Diagram
IT20382476 | Perera P.V.Y| 2023-044

## Slide 38: Technologies
IT20382476 | Perera P.V.Y | 2023-044
Technologies
Python
TensorFlow
OpenCV
ROS
Qgis
Keras
Vscode
Google Colab

## Slide 39: Requirements
IT20382476 | Perera P.V.Y | 2023-044
Functional Requirements
Non-Functional Requirements
  Adaptability
  Detecting the center of the path
  Image Thresholding and preprocessing data accurately.
  Calculate the angle to detect the center of the path
  Performance
  Efficient
  Accuracy
  Develop and Counter Extraction

## Slide 40
Work Breakdown Structure
IT20382476 | Perera P.V.Y| 2023-044
Completed
To Be Completed
Tea Stem Identification
Planning
Identifying requirements
Identifying Algorithm & function
Identifying the technologies
Allocating timeframe
Dataset Creation
Collecting the dataset
Data preprocessing
Labeling
Model Development
Using Unet architecture
Evaluating the performance
Optimizing the model & offload inferencing
Testing & Validation
Testing the performance in various scenarios
Data Transfer
Transfer the angle
Test the robot in actual environment
Finetune the model based on current performance

## Slide 41
Evaluation
IT20382476 | Perera P.V.Y.| 2023-044

## Slide 42: Gannt Chart
IT20382476 | Perera P.V.Y | 2023-044

## Slide 43: References
[1] D. Aghi, S. Cerrato, V. Mazzia, and M. Chiaberge, “Deep Semantic Segmentation at the Edge for Autonomous Navigation in Vineyard Rows,” IEEE Int. Conf. Intell. Robot. Syst., pp. 3421–3428, 2021, doi: 10.1109/IROS51168.2021.9635969.
[2] S. Bonadies and S. A. Gadsden, “An overview of autonomous crop row navigation strategies for unmanned ground vehicles,” Eng. Agric. Environ. Food, vol. 12, no. 1, pp. 24–31, 2019, doi: 10.1016/j.eaef.2018.09.001.
[3] S. Jaiswal and M. K. Pandey, “A Review on Image Segmentation,” Adv. Intell. Syst. Comput., vol. 1187, pp. 233–240, 2021, doi: 10.1007/978-981-15-6014-9_27.
[4] T. Zhou, W. Wang, E. Konukoglu, and L. Van Goo, “Rethinking Semantic Segmentation: A Prototype View,” Proc. IEEE Comput. Soc. Conf. Comput. Vis. Pattern Recognit., vol. 2022-June, pp. 2572–2583, 2022, doi: 10.1109/CVPR52688.2022.00261.
[5] T. T. P. Quoc, T. T. Linh, and T. N. T. Minh, “Comparing U-Net Convolutional Network with Mask R-CNN in Agricultural Area Segmentation on Satellite Images,” Proc. - 2020 7th NAFOSTED Conf. Inf. Comput. Sci. NICS 2020, pp. 124–129, 2020, doi: 10.1109/NICS51282.2020.9335856.
IT20382476 | Perera P.V.Y | 2023-044

## Slide 44: IT20265410 Premathilake H.T.M Information Technology
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 45
INTRODUCTION
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 46
Background
What is stem identification?
How to identify the stem? [1],[2]
How stem identification works?
How does stem identification helps "TeaBot" to do feralization process?
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 47: Research Gap
Not exclusively focused on the tea plantation and preservation.
Studies have not been conducted to identify the end of the tea stem [3],[4],[5],[6].
Not aligned with the liquid fertilizing process.
Identify the variability in tea stem growth patterns.
Use machine learning techniques, compared to other methodologies.
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 48: Research Question
How to give the coordinates of the end of the tea stem in order to fulfill the liquid fertilizing process?
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 49
OBJECTIVES
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 50: Specific and Sub Objectives
Main Objective
Develop an image processing algorithm to precisely identify the end of the stem and pass the coordinators to the liquid spraying controller.
Sub-Objectives
  Gathered dataset and apply preprocessing techniques
  Developing, testing and optimizing the image processing model
  Developing a lightweight model based on ResNet50 to run on Raspberry Pi
  Transfer data to liquid spraying controller
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 51
METHODOLOGY
IT20265410 | Premathilake H.T.M | 2023-044
System Overview Diagram
Technologies
Requirements
Work Breakdown Structure

## Slide 52: System Overview Diagram
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 53: Technologies
IT20265410 | Premathilake H.T.M | 2023-044
Technologies
Python
TensorFlow
OpenCV
ROS
Keras
Google Colab
ResNet Architecture

## Slide 54: Requirements
IT20265410 | Premathilake H.T.M | TMP-23-044
Functional Requirements
Non-Functional Requirements
  Adaptability
  Capability to get the correct coordinates
  Precisely identify the end of the tea stem
  Capability to pass the accurate coordinates to the liquid spraying controller
  Performance
  Efficient
  Accuracy

## Slide 55
Work Breakdown Structure
IT20265410 | Premathilake H.T.M | 2023-044
Completed
To Be Completed
Tea Stem Identification
Planning
Identifying requirements
Identifying Algorithm & function
Identifying the technologies
Allocating timeframe
Dataset Creation
Collecting the dataset
Data preprocessing
Labeling
Model Development
Using ResNet architecture
Developing a lightweight model
Optimizing the model
Testing & Validation
Testing and verifying accuracy
Validating the output result
Data Transfer
Integrating the ML model
Transferring the coordinators
Evaluating the performance

## Slide 56
Evaluation
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 57
Gantt Chart
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 58: References
[1] “Localised feature comparison between VGG-16 and ResNet-50. Although... | Download Scientific Diagram.” https://www.researchgate.net/figure/Localised-feature-comparison-between-VGG-16-and-ResNet-50-Although-both-models-extracted_fig6_328440990 (accessed May 11, 2023).
[2] “Accuracy and loss values for the VGG16 and ResNet50 models on the... | Download Scientific Diagram.” https://www.researchgate.net/figure/Accuracy-and-loss-values-for-the-VGG16-and-ResNet50-models-on-the-GAN-augmented-dataset_fig1_352142241 (accessed May 11, 2023).
[3] L. A. Wells and W. Chung, “Real-Time Computer Vision for Tree Stem Detection and Tracking,” For. 2023, Vol. 14, Page 267, vol. 14, no. 2, p. 267, Jan. 2023, doi: 10.3390/F14020267.​
[4] C. W. Bac, J. Hemming, and E. J. Van Henten, “Stem localization of sweet-pepper plants using the support wire as a visual cue,” Comput. Electron. Agric., vol. 105, pp. 111–120, Jul. 2014, doi: 10.1016/J.COMPAG.2014.04.011.​
[5] R. P. Haff, D. C. Slaughter, and E. S. Jackson, “X-Ray Based Stem Detection in an Automatic Tomato Weeding System,” Appl. Eng. Agric., vol. 27, no. 5, pp. 803–810, 2011, doi: 10.13031/2013.39559.​
[6] W. Wang, C. Li, K. Wang, L. Tang, P. F. Ndiluau, and Y. Cao, “Sugarcane stem node detection and localization for cutting using deep learning,” Front. Plant Sci., vol. 13, p. 5181, Dec. 2022, doi: 10.3389/FPLS.2022.1089961/BIBTEX.
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 59: IT20011970 Bamunusinghe G.P Software Engineering
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 60
INTRODUCTION
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 61: Background
IT20011970 | Bamunusinghe G.P | 2023-044
The movement of the robot arm and the liquid nozzles must be precisely controlled to ensure the accuracy and efficiency of the application.
The velocity of the robot affects the movement of the robotic arm’s movement of the liquid nozzles, and this must be taken into account in the control system.
PID control is a widely used method for fine-tuning the movement of robotic arms[5], including the movement of liquid nozzles in liquid sprayer systems.
Regulating water pressure is also important to ensure consistent application, and detecting and responding to water blockages can prevent damage to crops and the environment.

## Slide 62
Research Gap
Most of spraying systems waste lots of water and efficiency is low [9].
There is no specific system to detect root and water them accurately.
There is no specific system to validate water spraying path.
For tea plants, misting fertilizer is not recommended.
Most of the systems do not have stabilizing water spraying nozzles.
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 63: Research Question
How to water the plants precisely according to the coordinates with the relative velocity of the robot ?
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 64
OBJECTIVES
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 65
IT20011970 | Bamunusinghe G.P | TMP-23-044
Specific and Sub Objectives
Main Objective
To Develop the liquid nozzles controller of the TeaBot to liquid fertilize the tea plants more efficiently.
Sub-Objectives
  Develop the motor controlling for the nozzles with PID controls.
  Move the liquid nozzles to the exact spot with the given coordinates by the controller.
  Develop the nozzle movements with the given coordinates by computer vision
  To move the nozzles with the relative velocity of the robot.
  To regulate water pressure and, if water blocks occur, have the system turn itself off

## Slide 66
METHODOLOGY
System Overview Diagram
Technologies
Requirements
Work Breakdown Structure
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 67: System Overview Diagram
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 68
IT20011970 | Bamunusinghe G.P | 2023-044
Technologies
Technologies
Python
ROS
Algorithms
PID
Servo Motor Control
Raspberry Pi
Ubuntu
Solid Works
Angular
Arduino
Stabilizer

## Slide 69: Requirements
Functional Requirements
Non-Functional Requirements
  Accuracy
  Performance
  Speed
  Water spraying to the stem
  Rotation of the water arm
  Water spraying angle control
  Water pressure control
  Reusability
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 70
IT20011970 | Bamunusinghe G.P | TMP-23-044
Liquid Sprayer
Arm & Hardware
Mechanical design
3D printing
Firmware
Assembling
Algorithm & Software
Ideation
Coding
Testing
Laser Tracker
Mechanical design
Hardware development
Assembling
Completed
To Be Completed
Work Breakdown Structure

## Slide 71
Evaluation
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 72
IT20011970 | Bamunusinghe G.P | 2023-044
Gannt Chart

## Slide 73: References
IT20011970 | Bamunusinghe G.P | 2023-044
[1]A. Shilpa, V. Muneeswaran, and D. Devi Kala Rathinam, “A Precise and Autonomous Irrigation System for Agriculture: IoT Based Self Propelled Center Pivot Irrigation System,” 2019 5th Int. Conf. Adv. Comput. Commun. Syst. ICACCS 2019, pp. 533–538, Mar. 2019, doi: 10.1109/ICACCS.2019.8728550.
[2] a G. Smajstrla et al., “Efficiencies of Florida Agricultural Irrigation Systems,” BUL247, Univ. Florida, no. July 2002, p. 14, 2002.
[3] A. Heideker, D. Ottolini, I. Zyrianoff, A. T. Neto, T. Salmon Cinotti, and C. Kamienski, “IoTbased Measurement for Smart Agriculture,” 2020 IEEE Int. Work. Metrol. Agric. For. MetroAgriFor 2020 - Proc., pp. 68–72, 2020, doi: 10.1109/MetroAgriFor50201.2020.9277546.
[4] D. Cooley, R. M. Maxwell, and S. M. Smith, “Center Pivot Irrigation Systems and Where to Find Them: A Deep Learning Approach to Provide Inputs to Hydrologic and Economic Models,” Front. Water, vol. 3, Dec. 2021, doi: 10.3389/frwa.2021.786016.
[5] C. Cruz Ulloa, A. Krus, A. Barrientos, J. del Cerro, and C. Valero, “Robotic Fertilization in Strip Cropping using a CNN Vegetables Detection-Characterization Method,” Comput. Electron. Agric., vol. 193, no. January, p. 106684, 2022, doi: 10.1016/j.compag.2022.106684.
[6]“Greenhouse Irrigation - What’s the best watering system? | Greenhouse Emporium.” https://greenhouseemporium.com/blogs/greenhouse-gardening/greenhouse-irrigationsystems/ (accessed Mar. 20, 2023).

## Slide 74
Demonstration

## Slide 75
IT19973470 | Gunawardana I.I.E | 2023-044
IT19973470 Gunawardana I.I.E Software Engineering

## Slide 76: IT20382476 Perera P.V.Y Data Science
IT20382476 | Perera P.V.Y | 2023-044

## Slide 77: IT20265410 Premathilake H.T.M Information Technology
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 78: IT20011970 Bamunusinghe G.P Software Engineering
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 79
Q & A

## Slide 80
THANK YOU!