## Slide 1: TeaBot
Tea Plantation Preservation Using an Intelligent Robot

## Slide 2
Supervisor:
Ms. Shashika Lokuliyana
Co-Supervisor:
Ms. Narmada Gamage
External Supervisor:
Mr. Rajitha de Silva
IT19973470 Gunawardana I.I.E
IT20382476 Perera P.V.Y
IT20265410 Premathilake H.T.M
IT20011970 Bamunusinghe G.P
Team

## Slide 3
TeaBot is a well developed autonomous robot to replace the human resource
Watering and fertilizing for tea estates. (Liquid fertilization)
Operate in off road conditions
No need a highly arranged clear paths to navigate.
Increasing the efficiency and decrease the water and fertilizer wastage.
TeaBot can identify the path to navigate and identify the end of the plant stems and liquid fertilizing the plants efficiently.
Introducing TeaBot…

## Slide 4
How to develop the TeaBot for the liquid fertilization process efficiently?
Research Problem

## Slide 5
Objectives
Develop the robot controller of the TeaBot to navigate in off-road conditions with the computer vision guidance.
The development of the computer vision algorithm to navigate the robot automatically in the tea plantation rows in varying environmental conditions
Develop a computer vision algorithm to precisely identify the end of the tea stem and pass the coordinators to the liquid spraying controller.
Develop the liquid nozzles controller of the TeaBot to liquid fertilize the tea plants more efficiently.

## Slide 6
System Overview Diagram

## Slide 8
Robot Operating System
Why we use ROS? | Without ROS
Cooperate the components with low coupling and reduce the dependencies | have the possibilities to communicate the components
Can create the components separate. Each component is called as a node | Difficult to update the components since it has no proper convention to cooperate
nodes are communicating with ROS topics to send and receive data among the components | In programming, called it as low coupling high cohesion
Nodes are performing as publisher and subscriber | reduce the dependency level of the components
similar to the process of MQTT protocol | 

## Slide 9
Twist Library
Why we use Twist? | Without Twist
Capable to provide the linear velocity and the angle to the ROS node | Have the possibilities to provide velocity and the angle by creating a custom python class
Pass the linear velocities for the x, y, z directions | But arising problems when connecting the nodes because of custom classes.
Pass the angles for the x, y, z directions | Not maintaining a convention to communicate among nodes
Robot controller’s data in and out are defined by the Twist library | 
Can create a separate node with Twist library to provide the linear and angles to the robot controller | 
No need to change any coding level of the robot controller | 
Twist is a convention | 
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 10
System Overview

## Slide 11
System Components
Motor Controller
Arduino
Arm Controller
Arduino
Pump Controller
Arduino
Raspberry Pi
Ubuntu PC
3 Cameras
USB
USB
USB
ROS Wifi

## Slide 12
ROS Nodes Graphs

## Slide 13
What is liquid fertilization?

## Slide 15: Budget
Item | Quantity | Amount (LKR)
Rubber wheels | 4 | 4,000
Sprocket, chain and wheel (gear system) | 4 | 10,800
Iron frame | 1 | 15,500
Motors | 4 | 14,000
43A Motor drivers | 4 | 5,400
Raspberry Pi | 1 | 90,000
12V 65Ah battery | 1 | 45,000
12V 8Ah battery | 1 | 5,000
Camera | 3 | 15,000
Liquid nozzles | 2 | 3,000
Servo motors | 8 | 9,600
Total |  | 220,000

## Slide 16
IT20011970 | Bamunusinghe G.P | 2023-044
Gannt Chart

## Slide 17
IT19973470 | Gunawardana I.I.E | 2023-044
IT19973470 Gunawardana I.I.E Software Engineering

## Slide 18
Background & Literature
How to drive the robot?
How to do the power management of the robot?
How to operate the robot with Raspberry Pi and Arduino?
How to operate the robot with ROS?
How will the path navigation drive the robot autonomous?
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 19: Research Problem
How to navigate the TeaBot efficient in off-road conditions with the computer vision guidance and maintain the power more effective?
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 20: Specific and Sub Objectives
Main Objective
    Develop the robot controller of the TeaBot to navigate in off-road conditions with the computer vision guidance.
Sub-Objectives
    Design the robot chassis to easily drive, easy to handle and consume low power and low cost to build.
    Navigate the robot with the Twist library for the given linear velocity to go forward and backward and angles to steer.
    Read the coordinates given by the computer vision to navigate the robot in the track and manual control if needed.
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 21
Hardware - Robot Chassis
6 inches wheels – 4
Wiper motors (2 to 10 amps) – 4
Bicycle sprocket wheels (18 and 16) – 4
Bicycle chains – 4
Box bar + flat iron
BTS7960 motor drivers – 4
Arduino Nano – 1
Raspberry Pi 4 – 1
12V 35A battery
12V 8A battery
Cost – Rs. 178000
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 22
Hardware - Robot Chassis
Move forward or backward
Set the speed to drive (Twist)
Steering according to the given angles
Turn left or right while driving forward or backward (Twist)
Skid steer to left or right
Smooth driving
Optimized to protect the motors from sudden start or stop
One dedicated battery for the motors for the maximum power
Another dedicated battery for the drivers + Arduino + raspberry for a better performance
Tested in a hard environment
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 23
Robot Chassis Size – 21 inches x 28 inches
0.3 m/s robot speed and carry 40kg
Uses 6 inches wheels and will change to 8 inches mud wheels
The motors are wiper motors since it is low speed, high torque and can carry large weight without getting stuck
The power distribution done by chain sprocket system to get the maximum torque
If the motors directly connect, need to add large wheels to increase ground clearance. The robot weight directly impact to the motor armature
Used 2 x 45A max motor drivers
Used Raspberry pi and Arduino nano with ROS Noetic for processing
IT19973470 | Gunawardana I.I.E | 2023-044
Hardware - Robot Chassis

## Slide 24
IT19973470 | Gunawardana I.I.E | 2023-044
System Overview Diagram

## Slide 25
Serial
Power Line (35A)
Power Line (8A)
Power Line (8A)
Power Line (35A)
Data Line
Data Line
PWM Line
PWM Line
Power Line (8A)
Robot Controller Node (Subscriber)
12V 35Ah
Power Line (8A)
12V 8Ah
Motor Left Front
BTS7960 Motor Driver (Left)
BTS7960 Motor Driver (Right)
Motor Left Rear
Motor Right Front
Motor Right Rear
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 26
Tea Row
Tea Row
Twist Remote
θ
-θ
+
-
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 27
Left Motor Driver
Right Motor Driver
Arduino Nano
Raspberry Pi
ROS Motor Controller Node
Twist
Velocity
Max 0.3 m/s
Angles
Computer Vision Path Navigation
ROS Wifi
Serial Communication
Motor 1
Motor 2
Motor 3
Motor 4
Algorithm
Algorithm
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 28
Left Motor Driver
Right Motor Driver
Arduino Nano
Raspberry Pi
ROS Motor Controller Node
Twist
Velocity
Max 0.3 m/s
Angles
Computer Vision Path Navigation
ROS Wifi
I2C Communication
Motor 1
Motor 2
Motor 3
Motor 4
Arduino Nano
IT19973470 | Gunawardana I.I.E | 2023-044
Possible Solution

## Slide 29
Left Motor Driver
Right Motor Driver
Arduino Nano
Raspberry Pi
ROS Motor Controller Node
Twist
Velocity
Max 0.3 m/s
Angles
Computer Vision Path Navigation
ROS Wifi
Serial Communication
Motor 1
Motor 2
Motor 3
Motor 4
Arduino Nano
Serial Communication
IT19973470 | Gunawardana I.I.E | 2023-044
Possible Solution

## Slide 30
L
L
R
R
L
R
L
R
L
R
L
R
0ms
300ms
600ms
900ms
1200ms
0ms
300ms
600ms
900ms
1200ms
Motor Controlling for time frames
Previous
After
Developed Solution
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 31
Left Motor Driver
Right Motor Driver
Arduino Nano
Raspberry Pi
ROS Motor Controller Node
Twist
Velocity
Max 0.3 m/s
Angles
Computer Vision Path Navigation
ROS Wifi
Serial Communication
Motor 1
Motor 2
Motor 3
Motor 4
Algorithm
Algorithm
IT19973470 | Gunawardana I.I.E | 2023-044
Developed Solution

## Slide 32
IT19973470 | Gunawardana I.I.E | 2023-044
Max velocity – 0.3 m/s
Angle -> 15 pixels – 150 pixels
(15 < angle < 150)
PWM = (velocity / max velocity) * 255
PWM angle = PWM – ((angle – 15) / 15)
If angle > 0 then right
If angle < 0 then left
If robotGo = 1 then Go forward
If robotGo = 2 then Go backward
If robotGo = 3 then Turn right
If robotGo = 4 then Turn left
[left, right, robotGo, pwmDelay, pwmDelayLevel, 1, 1]

## Slide 33
Pass by Integer
Can pass by in integer data type
Pass values one after another
Difficult to synchronize
Takes much time to pass an array
Make more errors
No need any logic at receiver side to read values
IT19973470 | Gunawardana I.I.E | 2023-044
Pass by String
Can pass by in String data type
Pass values once as a String by comma separated
Much easy to synchronize
Less errors
Takes very low time to pass an array
Need a logic at the receiver side to read values
Conclusion
Consider only the data transfer speed and less errors
Pass by String is the best
Serial Communication

## Slide 34
Arduino Nano
Single Thread
Left
0
255
255
200
Right
0
255
100
120
0 – 150 delay (Start motors)
150 – 0 delay (Stop motors)
In a Single thread without time delay,
Can control the two motors one after another quickly, since the loop is very fast. No delays occurred.
But this is not good for this setup, since the motors are carrying a heavy weight and this scenario will damage the motors.
In a single thread with a time delay,
Cannot control the two motors one after another quickly,
Since the loop is slow now because of the delays.
Designed a separate motor controlling algorithm to operate two motors parallelly.
Now motors are protected and can operate all motors simultaneously in a single-threaded environment.
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 35
IT19973470 | Gunawardana I.I.E | 2023-044
ROS Node

## Slide 36
METHODOLOGY
Work Breakdown Structure @PP1
Work Breakdown Structure @PP2
Technologies
Requirements
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 37
Work Breakdown Structure @PP1
Robot Controller
Motor Controller
Make the robot structure
Autopilot
Provide computer vision coordinates
Remote Controller
Path End Detection
Develop the algorithm
IT19973470 | Gunawardana I.I.E | 2023-044
Make the power supply
Create the motor driving
Twist library to linear and angular movements
Completed
To Be Completed
Angular app for remote development
Create the communication
Testing the performance in various scenarios
Drive
Drive the robot by providing PWM values
Drive the robot forward, backward, steer left and right
Drive it in off road conditions to test
Drive the robot with Twist library
Test the robot autopilot
Finetune the algorithm based on performance

## Slide 38
Work Breakdown Structure @PP2
Robot Controller
Motor Controller
Make the robot structure
Autopilot
Provide computer vision coordinates
Remote Controller
Path End Detection
Develop the algorithm
IT19973470 | Gunawardana I.I.E | 2023-044
Make the power supply
Create the motor driving
Twist library to linear and angular movements
Completed
To Be Completed
Angular app for remote development
Create the communication
Testing the performance in various scenarios
Drive
Drive the robot by providing PWM values
Drive the robot forward, backward, steer left and right
Drive it in off road conditions to test
Drive the robot with Twist library
Test the robot autopilot
Finetune the algorithm based on performance

## Slide 39: Technologies
Technologies
Python
ROS Noetic
Algorithms
Twist to PWM
Motor Control
Angular
Ubuntu 20.04
MQTT
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 40: Requirements
IT19973470 | Gunawardana I.I.E | 2023-044
Functional Requirements
Non-Functional Requirements
  Efficient
  Easy to handle
  Navigate the robot forward and backward
  Driving the robot with the computer vision coordinates
  Drive the robot in manual mode
  Performance

## Slide 41
Chart: Time vs pwm
| 0ms | 300ms | 600ms | 900ms | 1200ms | 1500ms
Series 1 | 255 | 255 | 150 | 0
Previous
IT19973470 | Gunawardana I.I.E | 2023-044
Results & Discussion

## Slide 42
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 43
Chart: Time vs pwm
| 0ms | 300ms | 600ms | 900ms | 1200ms | 1500ms | 1800ms | 2100ms
Series 1 | 255 | 255 | 150 | 0
After
IT19973470 | Gunawardana I.I.E | 2023-044
Results & Discussion

## Slide 44
Conclusion
IT19973470 | Gunawardana I.I.E | 2023-044
Motors are protected and can operate all motors simultaneously in a single-threaded environment.
Consider only the data transfer speed and less errors.
Pass by String is the best for serial communication.

## Slide 45: References
[1] L. Grimstad and P. J. From, “Thorvald II - a Modular and Re-configurable Agricultural Robot,” IFAC-PapersOnLine, vol. 50, no. 1, pp. 4588–4593, 2017, doi: 10.1016/j.ifacol.2017.08.1005.
[2] Cihan YURTSEVER, Y. ERTAS, O. SUSTAM, and C. ULU, “Development of an Agriculture Robot for Row-type Seed Sowing Applications,” J. Selcuk. Spec. Issue 2020 (ICAT’20, vol. 2020, pp. 228–242, 2020.
[3] E. P. Godoy, G. T. Tangerino, R. A. Tabile, R. Y. Inamasu, and A. J. V. Porto, “Networked control system for the guidance of a four-wheel steering agricultural robotic platform,” J. Control Sci. Eng., vol. 2012, 2012, doi: 10.1155/2012/368503.
[4] P. Biber, U. Weiss, M. Dorna, and A. Albert, “Navigation System of the Autonomous Agricultural Robot ‘BoniRob,’” Work. Agric. Robot. Enabling Safe, Effic. Afford. Robot. Food Prod., pp. 1–7, 2012.
[5] T. Mueller-Sim, M. Jenkins, J. Abel, and G. Kantor, “The Robotanist: A ground-based agricultural robot for high-throughput crop phenotyping,” Proc. - IEEE Int. Conf. Robot. Autom., pp. 3634–3639, 2017, doi: 10.1109/ICRA.2017.7989418.
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 46: IT20382476 Perera P.V.Y Data Science
IT20382476 | Perera P.V.Y | 2023-044

## Slide 47: Background & Literature
What is Automatic path detection?
How does Automatic path detection work?
How does Automatic Path detection help “TeaBot” to navigate ?[1][2]
How does Automatic Path Detection relate to ?[1][2]
IT20382476 | Perera P.V.Y | 2023-044

## Slide 48: Research Problem
How can a suitable algorithm be created to detect the path and address TeaBot’s navigation problem ?[1][2][3][4][5]
IT20382476 | Perera P.V.Y | 2023-044

## Slide 49: Specific and Sub Objectives
Main Objective
Develop an algorithm to precisely detect the navigation path.
Sub-Objectives
  Implement an algorithm to accurately detect the center of path.
    Develop a Classic Computer Vision algorithm to segment the input frame.
    Algorithm creation to detect center of the path.
  Test and validate the performance in various scenarios and fine-tune the algorithm.
IT20382476 | Perera P.V.Y | 2023-044

## Slide 50: System Overview Diagram
IT20382476 | Perera P.V.Y| 2023-044

## Slide 51: Possible Solution
IT20382476 | Perera P.V.Y| 2023-044
Segmentation model to detect the center of path.
  PP1 developed a U-Net model.
  Finetuned the model.
Potential problems identified.
  Inaccurate results for noisy images.
  Lengthy output processing times.
  Exhibited substantial resource consumption.
Possible solution : Classic computer vision approach

## Slide 52: Developed Solution
Capturing a frame from the video through the webcam
Output segmented image using computer vision
Algorithm development for path identification
Pass the error to the robot controller
Calculating the position error
IT20382476 | Perera P.V.Y | 2023-044

## Slide 53
IT20382476 | Perera P.V.Y.| 2023-044
ROS Node

## Slide 54
METHODOLOGY
Work Breakdown Structure @PP1
Work Breakdown Structure @PP2
Technologies
Requirements
IT20382476 | Perera P.V.Y.| 2023-044

## Slide 55
Work Breakdown Structure @PP1
IT20382476 | Perera P.V.Y| 2023-044
Completed
To Be Completed
Path Identification
Planning
Identifying requirements
Identifying Algorithm & function
Identifying the technologies
Allocating timeframe
Dataset Creation
Collecting the dataset
Data preprocessing
Labeling
Model Development
Using Unet architecture
Evaluating the performance
Optimizing the model & offload inferencing
Testing & Validation
Testing the performance in various scenarios
Data Transfer
Transfer the position
Test the robot in actual environment
Finetune the model based on current performance

## Slide 56
Planning
Identifying requirements
Identifying Algorithm & function
Deep Learning Based Algorithm
Using U-Net architecture
Optimizing the model & offload inferencing
Identifying the technologies
Dataset Creation
Computer Vision Algorithm
Testing & Validation
Data Transfer
Allocating timeframe
Collecting the dataset
Data preprocessing
Image transfer algorithm
Detecting the center of the path
Testing the performance in various scenarios
Finetune the model based on performance
Transfer positional error
Test the robot in actual environment
Data labeling
Performance evaluation
Testing the new algorithm
Work Breakdown Structure @PP2
IT20382476 | Perera P.V.Y| 2023-044
Completed
To Be Completed
Path Identification

## Slide 57: Technologies
IT20382476 | Perera P.V.Y | 2023-044
Technologies
Python
TensorFlow
OpenCV
ROS
Qgis (Labling Tool)
Keras
VScode
Google Colab

## Slide 58: Requirements
IT20382476 | Perera P.V.Y | 2023-044
Functional Requirements
Non-Functional Requirements
  Adaptability
  Detecting the center of the path.
  Developing a Computer vision algorithm.
  Performance
  Efficient
  Accuracy
  Calculating the positional error.

## Slide 59: Results & Discussion
IT20382476 | Perera P.V.Y| 2023-044
Deep Learning Approach: U-Net Segmentation model
(a)
Accurate Results
(b)
Inaccurate Results

## Slide 60: Results & Discussion
IT20382476 | Perera P.V.Y| 2023-044
Drawbacks in Deep Learning Approach
Process time of algorithm was relatively high.
  Around 4-5 seconds.
Low accuracy for noisy images.
U-Net model high resource consumption [5][6].

## Slide 61: Results & Discussion
IT20382476 | Perera P.V.Y| 2023-044
Classic Computer Vision Approach
Graphs were developed and further discussed.

## Slide 62: ACCURATE RESULT
IT20382476 | Perera P.V.Y| 2023-044
  X-axis = Column Index
  Y-axis = White pixel count for each vertical range of columns.

## Slide 63
IT20382476 | Perera P.V.Y| 2023-044
Graph Developed for INACCURATE RESULT

## Slide 64
IT20382476 | Perera P.V.Y| 2023-044
Characteristics of the Graphs
Scenario | Characteristics of Graphs. | Example Graph
Accurate Results | Mean shifted double Gaussian curve IS VISIBLE | 
Inaccurate Results | Mean shifted double Gaussian curve NOT VISIBLE Scenarios - Paths having small tea plantations HSV color tunning will optimize performance | 

## Slide 65: Conclusion
IT20382476 | Perera P.V.Y| 2023-044
The classic computer vision-based method is more suitable for addressing the automatic navigation problem.
  Low resource consumption.
  More accurate results.
  Low-cost method.
Further optimizations are made to the algorithm.
  HSV color tunning will perform for frames having low density of plantations.

## Slide 66: References
[1] D. Aghi, S. Cerrato, V. Mazzia, and M. Chiaberge, “Deep Semantic Segmentation at the Edge for Autonomous Navigation in Vineyard Rows,” IEEE Int. Conf. Intell. Robot. Syst., pp. 3421–3428, 2021, doi: 10.1109/IROS51168.2021.9635969.
[2] S. Bonadies and S. A. Gadsden, “An overview of autonomous crop row navigation strategies for unmanned ground vehicles,” Eng. Agric. Environ. Food, vol. 12, no. 1, pp. 24–31, 2019, doi: 10.1016/j.eaef.2018.09.001.
[3] S. Jaiswal and M. K. Pandey, “A Review on Image Segmentation,” Adv. Intell. Syst. Comput., vol. 1187, pp. 233–240, 2021, doi: 10.1007/978-981-15-6014-9_27.
[4] T. Zhou, W. Wang, E. Konukoglu, and L. Van Goo, “Rethinking Semantic Segmentation: A Prototype View,” Proc. IEEE Comput. Soc. Conf. Comput. Vis. Pattern Recognit., vol. 2022-June, pp. 2572–2583, 2022, doi: 10.1109/CVPR52688.2022.00261.
[5] T. T. P. Quoc, T. T. Linh, and T. N. T. Minh, “Comparing U-Net Convolutional Network with Mask R-CNN in Agricultural Area Segmentation on Satellite Images,” Proc. - 2020 7th NAFOSTED Conf. Inf. Comput. Sci. NICS 2020, pp. 124–129, 2020, doi: 10.1109/NICS51282.2020.9335856.
[6] R. Jacobs et al., “Performance and limitations of deep learning semantic segmentation of multiple defects in transmission electron micrographs,” Cell Reports Phys. Sci., vol. 3, no. 5, pp. 1–50, 2022, doi: 10.1016/j.xcrp.2022.100876.
IT20382476 | Perera P.V.Y | 2023-044

## Slide 67: IT20265410 Premathilake H.T.M Information Technology
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 68
Background & Literature
What is stem identification?
How to identify the stem? [1],[2]
How stem identification works?
How does stem identification helps "TeaBot" to do feralization process?
Not exclusively focused on the tea plantation and preservation.
Studies have not been conducted to identify the the tea stem [3],[4],[5],[6].
Not aligned with the liquid fertilizing process.
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 69: Research Problem
How to give the coordinates of the detected tea stem through the developed algorithm in order to fulfill the liquid fertilizing process?
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 70: Specific and Sub Objectives
Main Objective
    Develop an algorithm to detect the tea stem and pass the value to the liquid spraying controller.
Sub-Objectives
  Implement an algorithm to accurately detect the tea stem.
    Develop a Classic Computer Vision algorithm to segment the input frame.
    Algorithm creation to detect the tea stem.
  Test and validate the performance in various scenarios and fine-tune the algorithm.
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 71: System Overview Diagram
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 72: Possible Solutions
IT20265410 | Premathilake H.T.M | 2023-044
Image processing model to identify the tea stem
  PP1 developed a ResNet50 model.
  Resnet50 model was light weighted as MobileNetV2.
Potential problems identified.
  Lengthy output processing times (4-5 seconds).
Possible solution : Classic computer vision approach

## Slide 73: Developed Solution
IT20265410 | Premathilake H.T.M | 2023-044
Capturing a frame from the video through the webcam
Output segmented image using computer vision
Algorithm development for stem identification
Pass the value to the water controlling node
Calculating the position of the stem

## Slide 74
IT20382476 | Perera P.V.Y.| 2023-044
ROS Node

## Slide 75
METHODOLOGY
IT20265410 | Premathilake H.T.M | 2023-044
Work Breakdown Structure @PP1
Work Breakdown Structure @PP2
Technologies
Requirements

## Slide 76
Work Breakdown Structure @PP1
IT20265410 | Premathilake H.T.M | 2023-044
Completed
To Be Completed
Planning
Identifying requirements
Identifying Algorithm & function
Identifying the technologies
Allocating timeframe
Dataset Creation
Collecting the dataset
Data preprocessing
Labeling
Model Development
Using ResNet50 architecture
Developing a lightweight model
Optimizing the model
Testing & Validation
Testing and verifying accuracy
Validating the output result
Data Transfer
Integrating the ML model
Transferring the coordinators
Evaluating the performance
Tea Stem Identification

## Slide 77
IT20265410 | Premathilake H.T.M | 2023-044
Planning
Identifying requirements
Identifying Algorithm & function
Image Processing Algorithm
Using ResNet50 architecture
Identifying the technologies
Dataset Creation
Computer Vision Algorithm
Testing & Validation
Data Transfer
Allocating timeframe
Collecting the dataset
Data preprocessing
Develop image transfer algorithm
Detecting the tea stem
Testing the performance in various scenarios
Testing
Transfer position value
Test the robot in actual environment
Data labeling
Developed a lightweight model
Finetune the algorithm based on performance
Work Breakdown Structure @PP2
Completed
To Be Completed
Tea Stem Identification

## Slide 78: Technologies
IT20265410 | Premathilake H.T.M | 2023-044
Technologies
Python
TensorFlow
OpenCV
ROS
Keras
Google Colab

## Slide 79: Requirements
IT20265410 | Premathilake H.T.M | TMP-23-044
Functional Requirements
Non-Functional Requirements
  Adaptability
  Capability to get the correct value
  Precisely identify the tea stem
  Capability to pass the accurate value to the liquid spraying controller
  Performance
  Efficient
  Accuracy

## Slide 80: Results & Discussion
IT20265410 | Premathilake H.T.M | 2023-044
Image Processing Approach
(a)
Accurate Results
(b)
Inaccurate Results

## Slide 81: Results & Discussion
IT20265410 | Premathilake H.T.M | 2023-044
Drawbacks in Image Processing Approach
MobileNetV2 resulted a lengthy output time.
  Around 4-5 seconds
Training MobileNetV2 from scratch on custom datasets is a challenge.

## Slide 82
IT20265410 | Premathilake H.T.M | 2023-044
Classic Computer Vision Approach
(a) Accurate Results
Results & Discussion

## Slide 83: ACCURATE RESULT
IT20265410 | Premathilake H.T.M | 2023-044
  X-axis = Column index
  Y-axis = Pixel value summation for each vertical column

## Slide 84
IT20265410 | Premathilake H.T.M | 2023-044
INACCURATE RESULT

## Slide 85
Conclusion
IT20265410 | Premathilake H.T.M | 2023-044
The classic computer vision-based method is more suitable for detecting the tea stem for utilizing the liquid fertilization process.
    Low resource consumption.
    Output is published withing 1 second.
    Low-cost method.
Further optimizations are made to the algorithm
    Color tunning for small plantations.
    Optimizing the edge detection algorithm.

## Slide 86: References
[1] “Localised feature comparison between VGG-16 and ResNet-50. Although... | Download Scientific Diagram.” https://www.researchgate.net/figure/Localised-feature-comparison-between-VGG-16-and-ResNet-50-Although-both-models-extracted_fig6_328440990 (accessed May 11, 2023).
[2] “Accuracy and loss values for the VGG16 and ResNet50 models on the... | Download Scientific Diagram.” https://www.researchgate.net/figure/Accuracy-and-loss-values-for-the-VGG16-and-ResNet50-models-on-the-GAN-augmented-dataset_fig1_352142241 (accessed May 11, 2023).
[3] L. A. Wells and W. Chung, “Real-Time Computer Vision for Tree Stem Detection and Tracking,” For. 2023, Vol. 14, Page 267, vol. 14, no. 2, p. 267, Jan. 2023, doi: 10.3390/F14020267.​
[4] C. W. Bac, J. Hemming, and E. J. Van Henten, “Stem localization of sweet-pepper plants using the support wire as a visual cue,” Comput. Electron. Agric., vol. 105, pp. 111–120, Jul. 2014, doi: 10.1016/J.COMPAG.2014.04.011.​
[5] R. P. Haff, D. C. Slaughter, and E. S. Jackson, “X-Ray Based Stem Detection in an Automatic Tomato Weeding System,” Appl. Eng. Agric., vol. 27, no. 5, pp. 803–810, 2011, doi: 10.13031/2013.39559.​
[6] W. Wang, C. Li, K. Wang, L. Tang, P. F. Ndiluau, and Y. Cao, “Sugarcane stem node detection and localization for cutting using deep learning,” Front. Plant Sci., vol. 13, p. 5181, Dec. 2022, doi: 10.3389/FPLS.2022.1089961/BIBTEX.
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 87: IT20011970 Bamunusinghe G.P Software Engineering
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 88: Background & Literature
IT20011970 | Bamunusinghe G.P | 2023-044
The movement of the robot arm and the liquid nozzles must be precisely controlled to ensure the accuracy and efficiency of the application.
The velocity of the robot affects the movement of the robotic arm’s movement of the liquid nozzles, and this must be taken into account in the control system.
Stabilizer is a widely used method for fine-tuning the movement of robotic arms[5], including the movement of liquid nozzles in liquid sprayer systems.
Regulating water pressure is also important to ensure consistent application.

## Slide 89: Research Problem
How to water the plants precisely according to the coordinates with the relative velocity of the robot ?
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 90
IT20011970 | Bamunusinghe G.P | TMP-23-044
Specific and Sub Objectives
Main Objective
  To Develop the liquid nozzles controller of the TeaBot to liquid fertilize the tea plants more efficiently.
Sub-Objectives
  Develop the motor controlling for the nozzles with Stabilizer.
  Move the liquid nozzles to the exact spot with the given coordinates by the controller.
  Develop the nozzle movements with the given coordinates by computer vision
  To move the nozzles with the relative velocity of the robot.
  To regulate water pressure and, if water blocks occur, have the system turn itself off

## Slide 91
Hardware - Robot Arm
Arduino Nano – 1
Servo motors (NG 995) – 4
Water pump (R385) – 2
Stabilizer (MPU6050)– 2
LM785 converter – 2
Sprinkler – 2
Motor driver (L298) –1
Cost – Rs. 10,150
IT19973470 | Gunawardana I.I.E | 2023-044

## Slide 92: System Overview Diagram
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 93: Possible Solution
IT20011970 | Bamunusinghe G.P | 2023-044
Use looping motor control systems to water the plants.
    Use same movements to rotate motors.
    Speed of the pump is constant in each situation.
Potential problems identified.
    Water wastage.
    Low accuracy at water spraying.
Possible solution : Use computer vision approach to water plants

## Slide 94
Developed Solution
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 95
IT20382476 | Perera P.V.Y.| 2023-044
ROS Node

## Slide 96
METHODOLOGY
Work Breakdown Structure @PP1
Work Breakdown Structure @PP2
Technologies
Requirements
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 97
IT20011970 | Bamunusinghe G.P | TMP-23-044
Work Breakdown Structure @PP1
Liquid Sprayer
Arm & Hardware
Mechanical design
Arm design
Firmware
Assembling
Algorithm & Software
Ideation
Coding
Testing
Integration
Laser tracker
Hardware development
Assembling
Completed
To Be Completed
Tuning

## Slide 98
Work Breakdown Structure @PP2
IT20011970 | Bamunusinghe G.P | 2023-044
Liquid Sprayer
Arm & Hardware
Mechanical design
Arm design
Firmware
Assembling
Algorithm & Software
Ideation
Coding
Testing
Integration
Laser tracker
Hardware integration
Assembling
Tuning
Completed
To Be Completed

## Slide 99
IT20011970 | Bamunusinghe G.P | 2023-044
Technologies
Technologies
Python
ROS Noetic
Algorithms
Pixel count convert to servo angles
Servo Motor Control
Raspberry Pi
Ubuntu 20.0.4
Arduino
Stabilizer
OpenCV

## Slide 100: Requirements
Functional Requirements
Non-Functional Requirements
  Accuracy
  Performance
  Speed
  Water spraying to the stem
  Rotation of the water arm
  Water spraying angle control
  Water pressure control
  Reusability
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 101
IT20011970 | Bamunusinghe G.P | 2023-044
IT20011970 | Bamunusinghe G.P | 2023-044
Pixel count difference VS time gap
Low accuracy for pixel count difference between previous position and current position per second is more than 200.
For various scenarios Arm accuracy will depend on stem detection results.
Low accuracy in arm algorithm is identified for small tea plantations.
Results & Discussion

## Slide 102
Accuracy of the spraying arm according to the time gap VS Pixel count
IT20011970 | Bamunusinghe G.P | 2023-044
Time Gap (s) | Pixel count difference | Accuracy
1 | 100 | Accurate
1 | 200 | Accurate
1 | 300 | Not-Accurate
1 | 400 | Not-Accurate
1 | 500 | Not-Accurate
2 | 100 | Accurate
2 | 200 | Accurate
2 | 300 | Not-Accurate
2 | 400 | Not-Accurate
2 | 500 | Not-Accurate
3 | 100 | Not-Accurate
3 | 200 | Not-Accurate
3 | 300 | Not-Accurate
3 | 400 | Not-Accurate
3 | 500 | Not-Accurate
4 | 100 | Not-Accurate
4 | 200 | Not-Accurate
4 | 300 | Not-Accurate
4 | 400 | Not-Accurate
4 | 500 | Not-Accurate

## Slide 103: Graph Developed of RESULT
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 104: Conclusion
The classic computer vision-based spraying system is more suitable for watering plants.
    Low water wastage.
    Accurate water spraying.
Further optimizations are made to the arm.
    Laser tracker to control y axis of the robot.
    Tune variables to cancel noise.
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 105: References
IT20011970 | Bamunusinghe G.P | 2023-044
[1]A. Shilpa, V. Muneeswaran, and D. Devi Kala Rathinam, “A Precise and Autonomous Irrigation System for Agriculture: IoT Based Self Propelled Center Pivot Irrigation System,” 2019 5th Int. Conf. Adv. Comput. Commun. Syst. ICACCS 2019, pp. 533–538, Mar. 2019, doi: 10.1109/ICACCS.2019.8728550.
[2] a G. Smajstrla et al., “Efficiencies of Florida Agricultural Irrigation Systems,” BUL247, Univ. Florida, no. July 2002, p. 14, 2002.
[3] A. Heideker, D. Ottolini, I. Zyrianoff, A. T. Neto, T. Salmon Cinotti, and C. Kamienski, “IoTbased Measurement for Smart Agriculture,” 2020 IEEE Int. Work. Metrol. Agric. For. MetroAgriFor 2020 - Proc., pp. 68–72, 2020, doi: 10.1109/MetroAgriFor50201.2020.9277546.
[4] D. Cooley, R. M. Maxwell, and S. M. Smith, “Center Pivot Irrigation Systems and Where to Find Them: A Deep Learning Approach to Provide Inputs to Hydrologic and Economic Models,” Front. Water, vol. 3, Dec. 2021, doi: 10.3389/frwa.2021.786016.
[5] C. Cruz Ulloa, A. Krus, A. Barrientos, J. del Cerro, and C. Valero, “Robotic Fertilization in Strip Cropping using a CNN Vegetables Detection-Characterization Method,” Comput. Electron. Agric., vol. 193, no. January, p. 106684, 2022, doi: 10.1016/j.compag.2022.106684.
[6]“Greenhouse Irrigation - What’s the best watering system? | Greenhouse Emporium.” https://greenhouseemporium.com/blogs/greenhouse-gardening/greenhouse-irrigationsystems/ (accessed Mar. 20, 2023).

## Slide 106
Demonstration

## Slide 107
IT19973470 | Gunawardana I.I.E | 2023-044
IT19973470 Gunawardana I.I.E Software Engineering

## Slide 108: IT20382476 Perera P.V.Y Data Science
IT20382476 | Perera P.V.Y | 2023-044

## Slide 109: IT20265410 Premathilake H.T.M Information Technology
IT20265410 | Premathilake H.T.M | 2023-044

## Slide 110: IT20011970 Bamunusinghe G.P Software Engineering
IT20011970 | Bamunusinghe G.P | 2023-044

## Slide 111
Q & A

## Slide 112
THANK YOU!